## Slide 1: GEOS 38600/ GEOS 28600
Lecture 12
Monday 20 Feb 2017
Fluvial sediment transport: introduction

## Slide 2
REVIEW OF REQUIRED READING (SCHOOF & HEWITT 2013)
TURBULENT VELOCITY PROFILES, INITIATION OF MOTION
BEDLOAD, RIVER GEOMETRY
Fluvial sediment transport: introduction

## Slide 3
Re << 1  inertial forces unimportant  Stokes flow / creeping flow:
Schoof & Hewitt 2013
Ice sheets can have multiple stable equilibria for the same external forcing, with geologically
rapid transitions between equilibria

## Slide 4: Key points from today’s lecture
Critical Shields stress
Differences between gravel-bed vs. sand-bed rivers
Discharge-width scaling

## Slide 5: Prospectus: fluvial processes
Today: overview, hydraulics, initiation of motion, channel width adjustment.
Channel long-profile evolution.
Mountain belts.
Final lectures: landscape evolution (including fluvial processes.)
This section of the course draws on courses by W.E. Dietrich (Berkeley),
D. Mohrig (MIT  U.T. Austin), and J. Southard (MIT).

## Slide 6
REVIEW OF REQUIRED READING (SCHOOF & HEWITT 2013)
TURBULENT VELOCITY PROFILES, INITIATION OF MOTION
BEDLOAD, RIVER GEOMETRY
Fluvial sediment transport: introduction

## Slide 7: Hydraulics and sediment transport in rivers:
1) Relate flow to frictional resistance so can relate discharge to hydraulic geometry.
2) Calculate the boundary shear stress.
Parker Morphodynamics e-book
pool
Simplified geometry: average over a reach (12-15 channel widths).
 we can assume accelerations are zero.
 this assumption is better for flood flow (when most of the erosion occurs).
riffle
riffle
pool

## Slide 8: The assumption of no acceleration requires that gravity balances pressure gradients.
Dingman, chapter 6
τzx = ρgh sinθ
averaging over 15-20 channel widths
forces the water slope to ~ parallel the
basal slope

## Slide 9
τzx = ρgh sinθ
At low slope (S, water surface rise/run), θ ~ tan θ ~ sin θ
τb = ρgh S
0
τb
1
z/h
0
Frictional resistance:
L
w
h
Boundary stress = ρgh sinθ L w
Frictional resistance = τb L (w + 2 h)
ρgh sinθ L w = τb L (w + 2 h)
τb = ρgh ( w / (w + 2 h ) ) sinθ
Define hydraulic radius, R = hw / (w + 2 h)
 τb = ρgR sinθ
Basal shear stress, frictional resistance, and hydraulic radius
In very wide channels, R  h (w >> h)

## Slide 10
Law of the wall, recap:
τzx = ρ KT (du/dz)
τzx = μ(T,σ) (du/dz)
Glaciers ( Re << 1):
Rivers ( Re >> 1, fully turbulent):
eddy viscosity, “diffuses” velocity
KT = (k z )2 (du/dz)
From empirical & theoretical studies:
 τB = ρ(k z)2 (du/dz)2
 (τB /ρ )1/2 = k z (du / dz) = u* = “shear velocity”
 (ρ g h S /ρ )1/2 = u* = ( g h S )1/2
Now u* = k z (du / dz)
Separate variables: du = (u* / k z ) dz
Integrate: u = (u*/k) (ln z + c). For convenience, set c = -ln(z0)
Then, u = (u*/k) ln (z/z0)
(where k = 0.39-0.4 = von Karman’s constant)
“law of the wall”
(explained on next slide)
when z = z0, u = 0 m/s.
Memorize this.
Properties of turbulence:
Irregularity
Diffusivity
Vorticity
Dissipation

## Slide 11
Calculating river discharge, Q (m3s-1)
z0 is a length scale for grain roughness
varies with the size of the bedload. In this class, use
z0 = 0.12 D84, where D84 is the 84th
percentile size in a pebble-count (100th
percentile is the biggest).
Q = <u> w h
<u> = u(z) dz (1/(h-z0))
z0
h
<u> = (u*/k) (z0 + h ( ln( h / z0 ) – 1 ) ) (1/ (h - z0))
brackets denote vertical
average
u = (u*/k) ln (z/z0)
“law of the wall”
<u> = (u*/k) ln ( h / e z0)
<u> = (u*/k) ln (0.368 h / z0)
<u> = (u*/k) ( ln( h / z0 ) – 1 )
h >> z0:
typically rounded to 0.4
Extending the law of the wall
through the flow is a rough
approximation – do not use
this for civil-engineering
applications. This approach
does not work at all when
depth  clast grainsize.

## Slide 12
Drag coefficient for bed particles:
 τB = ρgRS = CD ρ <u>2 / 2
<u> = ( 2g R S / CD )1/2
( 2g / CD )1/2 = C = Chezy coefficient
<u> = C ( R S )1/2
Chezy equation (1769)
<u> = ( 8 g / f )1/2 ( R S )1/2
f = Darcy-Weisbach friction factor
<u> = R2/3 S1/2 n-1
3 alternative methods
n = Manning roughness coefficient
0.025 < n < 0.03 ----- Clean, straight rivers (no debris or wood in channel)
0.033 < n < 0.03 ----- Winding rivers with pools and riffles
0.075 < n < 0.15 ----- Weedy, winding and overgrown rivers
n = 0.031(D84)1/6 ---- Straight, gravelled rivers
In sand-bedded rivers (e.g. Mississippi), form drag due to sand dunes is important.
In very steep streams, supercritical flow may occur:
Froude number
Fr # = <u>/(gh)1/2 > 1
supercritical flow
Most used, because lots of investment in measuring n for different objects

## Slide 13
John Southard

## Slide 14
Sediment transport in rivers:
(Shields number)
FD
FL
F’g (submerged weight)
Φ
At the initiation of grain motion,
FD = ( F’g – FL ) tan Φ
 FD/F’g =
tan Φ
1 + (FL/FD) tan Φ
≈ τc D2
(ρs – ρ)gD3
= τc = τ*
(ρs – ρ)gD
Shields number (“drag/weight ratio”)
Is there a representative particle size for the bedload as a whole?
Yes: it’s D50.

## Slide 15: Equal mobility hypothesis
FD
FL
F’g (submerged weight)
Φ
Φ
D/D50
“Hiding” effect
small particles
don’t move significantly
before the D50 moves.
Significant controversy over validity of equal mobility hypothesis in the late ’80s – early ’90s.
Parameterise using
τ* = B(D/D50)α
α = -1 would indicate perfect equal mobility (no sorting by grain size with downstream distance)
α = -0.9 found from flume experiments (permitting long-distance sorting by grain size).
Trade-off between size and embeddedness

## Slide 16
Buffington & Montgomery, Water Resources Research, 1999
sand
gravel
τ*c50 ~ 0.04, from experiments (0.045-0.047 for gravel, 0.03 for sand)
1936:
1999:
Theory has approximately
reproduced some parts
of this curve.
Causes of scatter:
(1) differing definitions of
initiation of motion (most important).
(2) slope-dependence?
(Lamb et al. JGR 2008)
Hydraulically rough:
viscous sublayer is a thin
skin around the particles.
Re* = “Reynolds roughness number”

## Slide 17
REVIEW OF REQUIRED READING (SCHOOF & HEWITT 2013)
TURBULENT VELOCITY PROFILES, INITIATION OF MOTION
BEDLOAD, RIVER GEOMETRY
Fluvial sediment transport: introduction

## Slide 18: Consequences of increasing shear stress: gravel-bed vs. sand-bed rivers
John Southard
Suspension: characteristic velocity for
turbulent fluctuations (u*) exceeds
settling velocity (ratio is ~Rouse number).
Typical transport distance
100m/yr in gravel-bedded bedload
Sand: km/day
Empirically, rivers are either gravel-bedded or sand-bedded (little in between)
The cause is unsettled: e.g. Jerolmack & Brzinski Geology 2010 vs. Lamb & Venditti GRL 2016
(Experimentally, u* is approximately
equal to rms
fluctuations in vertical
turbulent velocity)

## Slide 19: Bedload transport
(Most common:)
qbl = kb(τb – τc)3/2
there is no theory for washload:
it is entirely controlled by upstream supply
Many alternatives, e.g.
Yalin
Einstein
Discrete element modeling
John Southard
Meyer-Peter Muller

## Slide 20: River channel morphology and dynamics
“Rivers are the authors of their own geometry” (L. Leopold)
  And of their own bed grain-size distribution.
Rivers have well-defined banks.
  Bankfull discharge 5-7 days per year; floodplains inundated every 1-2 years.
  Regular geometry also applicable to canyon rivers.
  Width scales as Q0.5
River beds are (usually) not flat.
  Plane beds are uncommon. Bars and pools, spacing = 5.4x width.
Rivers meander.
  Wavelength ~ 11x channel width.
River profiles are concave-up.
  Grainsize also decreases downstream.

## Slide 21
>20%; colluvial
Slope, grain size, and transport mechanism: strongly correlated
z
<0.1%
bar-pool
sand
bedload & suspension
0.1-3%
bar-pool
gravel
bedload
3-8%
step-pool
gravel
bedload
8-20%
boulder
cascade
(periodically
swept by
debris
flows)
rocks may be
abraded in place;
fine sediment bypasses boulders

## Slide 22: What sets width?
Eaton, Treatise on
Geomorphology, 2013
Q = wd<u>
w = aQb
d = cQf
<u> = kQm
b+f+m = 1
b = 0.5
m = 0.1
f = 0.4
Comparing
different points
downstream

## Slide 23
(1) Posit empirical relationships between hydraulics, sediment supply, and form (Parker et al. 2008 in suggested reading; Ikeda et al. 1988 Water Resources Research).
(2) Extremal hypotheses; posit an optimum channel, minimizing energy (Examples: minimum streampower per unit length; maximum friction; maximum sediment transport rate; minimum total streampower; minimize Froude number)
(3) What is the actual mechanism? What controls what sediment does, how high the bank is, & c.?
What sets width? Three approaches to this unsolved question:

## Slide 24: Key points from today’s lecture
Critical Shields stress
Differences between gravel-bed vs. sand-bed rivers
Discharge-width scaling