## Slide 1
Lecture 5
GEOS24705
History of Energy Use II

## Slide 2
Early uses of mechanical work from animals, wind, water
Grindstone, China from the encyclopedia “Tiangong Kaiwu”, by Song Yingxing (1637)
Vertical-axis waterwheel
1500s or earlier

## Slide 3
First recorded piston pump is in Renaissance
Grindstone, China from the encyclopedia “Tiangong Kaiwu”, by Song Yingxing (1637)
reproduction from: Donald Routledge Hill: A history of engineering in classical and medieval times
Taccola, 1450
Siena, Italy
De ingeneis 1433
(Concerning engines)
De machinis 1449
(Concerning machines)
but, pumps don’t replace bucket chains in England until 1700s

## Slide 4
Basic lift pump design basically unchanged
The lift pump
Animation from Scuola Media di Calizzano
Same technology used today in oil wells

## Slide 5
Heating: Large-scale wood-burning for industry
Georg Acricola “De res metallica”, Book XII (“Manufacturing salt, soda, alum, vitriol, sulphur, bitumen, and glass”), 1556.
D. Diderot & J. Le Rond d`Alembert eds, Encyclopédie méthodique. Paris 1763-1777 & 1783-87.

## Slide 6
“Lack of energy was the major handicap of the ancien régime economies”
--- F. Braudel, The Structures of Everyday Life
By the 18th century, Europe’s energy crisis limits growth
  18th century Europeans had complex and sophisticated technology, and an abundance of industrial uses for energy, but not enough supply

## Slide 7
“Within a few years after the commencement of the seventeenth century the change from wood fuel to coal, for domestic purposes, was general and complete.”
--- R. Galloway, A History of Coal Mining in Great Britain, 1882.
Wood  coal: changing an energy system
1600
Robert Allen, The British Industrial Revolution in Global Perspective

## Slide 8
The 2nd British energy crisis: flooding of the mines
1600s

## Slide 9
“The miners, no less than the smelters, had their difficulties during the seventeenth century, but of a totally different kind; for while the latter were suffering from too little fire, the former were embarrassed by too much water… the exhaustion of he coal supply was considered to be already within sight. In 1610, Sir George Selby informed Parliament that the coal mines at Newcastle would not last for the term of their leases of twenty-one years.”
--- R. Galloway, A History of Coal Mining in Great Britain, 1882.
The 2nd British energy crisis: flooding of the mines
1600s

## Slide 10
Fuel had become scarce even when only used for heat
Wood was insufficient, & coal was getting hard to extract
Surface “sea coal”  deep-shaft mining below the water table
2. There were limited ways to make motion
No way to make motion other than through capturing existing motion or through muscle-power
3. There was no good way to transport motion
Water and wind weren’t necessarily near demand
The 18th century European energy crisis has 3 parts

## Slide 11
“In the year 1708 a plan was projected in Scotland for draining collieries by means of windmills and pumps... one John Young, a millwright of Montrose... had been sent to Holland at the expense of the town to inspect the machinery there... Wind mills were erected at several collieries, but though they were powerful their action was found to be too intermittent; the mines being drowned and all the workmen thrown idle during long periods of calm weather. ”
--- R. Galloway, A History of Coal Mining in Great Britain, 1882.
Early complaints about intermittent renewables

## Slide 12
The heat to work barrier
the 18th century technological impasse
All technology involved only two energy conversions
Mechanical motion  mechanical motion
Chemical energy  heat
There was no way to convert chemical energy to motion other than muscles (human or animal)
– no engine other than flesh
The only means out of the energy crisis was coal
– but to mine the coal required motion for pumps.

## Slide 13
The revolutionary solution = break the heat  work barrier

## Slide 14
Newcomen “Atmospheric Engine”, 1712
The revolutionary solution = break the heat  work barrier
use heat to make ordered motion
(Note that widespread use & Industrial Revolution followed invention
by ~100 years – typical for energy technology)

## Slide 15
What is a “heat engine”?
  A device that generates converts thermal energy to mechanical work by exploiting a temperature gradient
  Makes something more ordered:
  random motions of molecules  ordered motion of entire body
  Makes something less ordered:
  degrades a temperature gradient (transfers heat from hot to cold)

## Slide 16
Hero of Alexandria, “Treatise on Pneumatics”, 120 BC
“lebes”: demonstration of lifting power of steam
“aeliopile”
Physics: long understood that steam exerted force
Evaporating water produces high pressure
Pressure = force / area

## Slide 17
Physics: condensing steam can produce suction force
Low pressure in airtight container means air exerts force
Same physics that lets you suck liquid through a straw

## Slide 18
First commercial use of steam:
the Savery engine
“A new Invention for Raiseing of Water and occasioning Motion to all Sorts of Mill Work by the Impellent Force of Fire which will be of great vse and Advantage for Drayning Mines, serveing Towns with Water, and for the Working of all Sorts of Mills where they have not the benefitt of Water nor constant Windes.”
Thomas Savery, patent application, filed 1698

## Slide 19
Savery engine is not a commercial success
“.. Savery’s engine was wholly unsuited for draining mines, and he failed to induce the miners to take it up. The greatest height to which it could raise water was.. not more than sixty or eighty feet...Moreover the miners [were]...afraid to introduce furnaces into their shafts, on account of ...their giving rise to explosions... ”
Robert Galloway, “A History of Coal Mining in Great Britain”

## Slide 20
Principles of Savery engine
Sucks water as one would with a straw
Heat water to make steam
Fill chamber with steam
Cool chamber, steam condenses
Pressure in chamber is now lower than atmospheric pressure
Open up valve connecting chamber to pipe in water
Atmospheric pressure causes water to flow up into chamber
Issues:
Good only for pumping liquids. Efficiency below 0.1%
Max pumping height: ~30 ft.
Why used at all? Because the coal was essentially free and the industry was desperate for a solution.
Notes: 2000 times less efficient than people or animals, but they cant eat coal.

## Slide 21
Newcomen’s design is state of the art for 60+ years
First true steam engine:
Thomas Newcomen, 1712, blacksmith
“It was at this juncture that the miners had put into their hands the most wonderful invention which human ingenuity had yet produced – the Newcomen steam-engine.. a machine capable of draining with ease the deepest mines; applicable anywhere; requiring little or no attention; so docile that its movements might be governed by the strength of a child; so powerful that it could put forth the strength of hundreds of horses; so safe that... the utmost damage that can come to it, is its standing still for want of fire.”
Robert Galloway, “A History of Coal Mining in Great Britain”

## Slide 22
Newcomen’s design is state of the art for 60 years
First true steam engine:
Thomas Newcomen, 1712, blacksmith
Copy of Papin’s engine of design of 1690
First reciprocating engine: linear motion of piston that transmits force
Steps
Fill chamber with steam
Cool the chamber to condense steam
Low pressure in chamber pulls piston down, lifts pump side
Open valve at bottom of piston, let gravity pull pump side down again
Steam fills chamber as piston rises
Issues:
Very low efficiency: 0.5%
Intermittent force transmission

## Slide 23
Newcomen’s design is state of the art for 60 years
First true steam engine:
Thomas Newcomen, 1712, blacksmith
Copy of Papin’s engine of design of 1690
First reciprocating engine: linear motion of piston that transmits force
Steps
Fill chamber with steam
Cool the chamber to condense steam
Low pressure in chamber pulls piston down, lifts pump side
Open valve at bottom of piston, let gravity pull pump side down again
Steam fills chamber as piston rises
Issues:
Very low efficiency: 0.5%
Intermittent force transmission

## Slide 24
Newcomen’s design is state of the art for 60 years
First true steam engine:
Thomas Newcomen, 1712, blacksmith
Copy of Papin’s engine of design of 1690
First reciprocating engine: linear motion of piston that transmits force
Steps
Fill chamber with steam
Cool the chamber to condense steam
Low pressure in chamber pulls piston down, lifts pump side
Open valve at bottom of piston, let gravity pull pump side down again
Steam fills chamber as piston rises
Issues:
Very low efficiency: 0.5%
Intermittent force transmission