## Slide 1
Lecture 6
GEOS24705
Steam engines, heat engines

## Slide 2
Newcomen’s design is state of the art for 60+ years
First true steam engine:
Thomas Newcomen, 1712, blacksmith
Copy of Papin’s engine of design of 1690
First reciprocating engine: linear motion of piston that transmits force
Issues:
Very low efficiency: 0.5%?
Intermittent force transmission

## Slide 3
Cooling towers from Cattenom nuclear power plant (heat from reactor drives a steam turbine)
All heat engines involve heat flow
No heat engine has perfect efficiency
All heat engines involve waste heat

## Slide 4
First modern steam engine:
James Watt, 1769 patent
(1774 production model)
Similar to Newcomen’s engine, but with steam now condensing in a separate condenser that is kept always cool.
In Newcomen’s engine, the metal cylinder would alternately heat and cool when filled with steam or when cooling water is added in condensing step.
In Watt’s engine, steam enters alternately at top and bottom of cylinder. As piston begins to move down, steam flushes into condenser where it condenses, providing the suction that is most of the force on the engine.
Lower fuel usage than Newcomen’s engine.

## Slide 5
First modern steam engine:
James Watt, 1769 (patent), 1774 (prod.)
Higher efficiency than Newcomen by introducing separate condenser
Reduces wasted heat by not heating and cooling entire cylinder

## Slide 6
Improved Watt steam engine:
James Watt, 1783 model
Albion Mill, London
As before:
Separate condenser
Improvements:
Force on both up- and downstroke
Continuous force transmission
Rotational motion
Engine speed regulator
Higher efficiency: ca. 3%
Engineers cared about efficiency –
coal = money
video of 1788 engine

## Slide 7
First locomotives – attempts to convert stationary steam engines
built by Richard Trevithick, mining engineer
Experimented with “high-pressure” steam (50 psi), double-acting cylinders.
1804 Pen-y-Darren locomotive, carrying iron in Wales, replacing horse-drawn tramway. Ran ~10 miles at ~2 mph but destroyed track.
Image: 1804 Coalbrookdale locomotive, which failed. No images of Pen-y-Darren survive

## Slide 8
Image: source unknown
First practical locomotives begin 1814
“Puffing Billy”, designed by William Hedley, (mine manager),
built by the mine’s blacksmith and enginewright
Coal hauler, 9” x 36” cylinders
Still basically a stationary steam engine placed on wheels

## Slide 9
First passenger locomotive, 1829
George Stephenson’s “Rocket”, built for Liverpool and Manchester Railway
won the Rainhill trials at 29 mph (unloaded), 14 mph loaded
first example of single pair of drive wheels
Image: source unknown
Stephenson was a mine engineman and brakeman, then enginewright. Illiterate til age 18. Built first locomotive in 1814.
Notes: Stephenson was a

## Slide 10
Piston pushed by steam on both up- and down-stroke.
No more need for a condenser. Steam is simply vented at high temperature
slide valve alternates input & exhaust
Double-acting steam engine

## Slide 11
Double-acting steam engine
slide valve alternates input & exhaust

## Slide 12
Double-acting steam engine
primary use: transportation

## Slide 13
Double-acting steam engine
What are benefits?
What are drawbacks?

## Slide 14
Double-acting steam engine
What are benefits?
Faster cycle – no need to wait for condensation. Can get more power, higher rate of doing mechanical work.
Also lighter and smaller – no need to carry a condenser around.
What are drawbacks?
Inefficiency – venting hot steam means you are wasting energy.
High water usage – since lose steam, have to keep replacing the water

## Slide 15
Double-acting steam engine:
Images top, left: Sandia Software
Image bottom: Ivan S. Abrams
water-intensive, fuel-intensive – requires many stops to take on water and fuel.

## Slide 16
History of locomotives
Central Pacific Railroad locomotive #173, Type 4-4-0, 1864
Image: Central Pacific Railroad Photographic History Museum

## Slide 17
History of locomotives
Northern Pacific Railway steam locomotive #2681, 1930
Image: Buckbee Mears Company, Photograph Collection ca. 1930, Location no. HE6.1N p11, Negative no. 25337. Source: Minnesota Historical Society